## Slide 1: Cache vs. Key-Dependency
Daniel Genkin, Romain Poussier, Rui Qi Sim, Yuval Yarom, and Yuanjing Zhao

## Slide 2: Introduction
Ciphers
  Vulnerable to cache attacks
  Recover secret information knowing the internal structure of cipher and victim cache accesses
Show that secret (key-dependent) transformations do NOT guarantee additional protection against cache attacks

## Slide 3: Pilsung
Part of Red-Star OS 3.0
Based on AES, with:
  Key-dependent S-Boxes
  Key-dependent “Shift-Rows” permutations
AES: Secret information can be recovered with cache attacks and knowing the internal structure of the cipher
Secret transformations do not make Pilsung secure against cache attacks used for AES

## Slide 4: AES Refresher
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
ADD-ROUND-KEY
SUB-BYTES
SHIFT-ROWS
MIX-COLUMNS
repeat
Plaintext,
Round-key,
Notes: 1 min

## Slide 5: Attacking AES
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
Input
Add-Round-Key
is the index to the S-Box.
If we can find index, we get the key.
Sub-Bytes
Notes: 30 sec

## Slide 6: Cache Attacks: Theory
Obtain S-Box accesses by observing memory accesses to the cache
PRIME+PROBE uses timing information to infer victim’s cache accesses over a period of time
Notes: 1.5 min

## Slide 7: Attack on AES
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
ADD-ROUND-KEY
SUB-BYTES
Plaintext,
Idea: Fix one plaintext byte
Fix S-Box access (observe in memory)
Get key byte using:
Round-key,
Notes: 1 min

## Slide 8: Cache Attacks: Practical Challenges
Limited temporal resolution
  Sample cache at regular intervals
  Many accesses happen between samples
  Solution: average over multiple encryptions
…
Notes: 2 minss

## Slide 9: Cache Attacks: Practical Challenges
Limited spatial resolution
  Can’t distinguish between accesses to the same cache line
    Multiple S-Box entries are present in the same cache line
    See S-Box accesses to the resolution of the cache line
      First round attack can only recover two to four bits of each key byte
  Solution: second round attack
… | … | … | …
S-Box (256 entries)
Cache
Notes: 2 minss

## Slide 10: Attack on AES
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
ADD-ROUND-KEY
SUB-BYTES
SHIFT-ROWS
MIX-COLUMNS
Plaintext,
Idea: Fix one plaintext byte
Fix S-Box access (observe in memory)
Get key byte using:
Limited spatial resolution: recover two to four bits
Round-key,
…
Cache
Access to part of the S-Box
Notes: 1 min

## Slide 11: Second Round Attack
🔑 |  |  | 
 | 🔑 |  | 
 |  | 🔑 | 
 |  |  | 🔑
🔑 |  |  | 
🔑 |  |  | 
🔑 |  |  | 
🔑 |  |  | 
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
ADD-ROUND-KEY
SUB-BYTES
SHIFT-ROWS
MIX-COLUMNS
plaintext
Idea: Fix four plaintext bytes
Result: four state bytes fixed at the end of the first round
Need to know transformations
Idea: Fix four plaintext bytes
that map to the same column after Shift-Rows

## Slide 12: Pilsung vs. AES
Based on AES with key-dependent transformations
Key schedule
  Master key is passed through a SHA1-based function to generating
  Uses AES key schedule with to generate eleven 128-bit round keys

## Slide 13: Pilsung vs. AES
S-Boxes
  Different S-Boxes are used for each state byte at each round
    16 different S-Boxes at each round
  The S-Boxes depend on the corresponding key byte of the next round
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
🔑 | 🔑 | 🔑 | 🔑
SUB-BYTES
AES
Pilsung
* patterns represent an S-Box

## Slide 14: Pilsung vs. AES
Shift-Rows
  Uses a pseudo-random permutation
  The permutation depends on the key of the next round
SHIFT-ROWS
AES
Pilsung
Next round key

## Slide 15: First Round Attack on Pilsung
Provides the two MSBs of each key byte
Use cache access patterns to infer S-Box access indices
Reduce search space for second round attack

## Slide 16: First Round Attack: Getting MSBs
…
…
…
…
Idea: S-Box index
Observe:
S-Box entries 0 – 63
  two MSBs: 00
Byte plaintext 64 – 127
  two MSBs: 01
  Key byte’s two MSBs = 01
Byte’s S-Box (256 entries)
Entries 0-63 (00xx xxxx2)

## Slide 17: First Round Attack: Getting MSBs
Idea: S-Box index
Observe:
S-Box entries 64 – 127
  two MSBs: 01
Byte plaintext 0 – 63
  two MSBs: 00
  Key byte’s two MSBs = 01
Byte’s S-Box (256 entries)
Entries 64-127 (01xx xxxx2)
Key byte’s two MSBs: 01
Key byte’s two MSBs: 01
…
…
…
…

## Slide 18: Preparing Second Round Attack: Reversing Shift-Rows
Shift-Rows permutation is key-dependent
Two steps for reversing Shift-Rows:
  Column mapping:
    Finding the group of four bytes that map to the same column in Shift-Rows
    Identify which column the group maps to
  Column ordering:
    Finding which row each byte goes to
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
SHIFT-
ROWS
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
? | ? | ? | ?
15 | ? | ? | ?
10 | ? | ? | ?
4 | ? | ? | ?
0 | ? | ? | ?
15 | ? | ? | ?
10 | ? | ? | ?
4 | ? | ? | ?
0 | ? | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
15 | 12 | ? | ?
10 | 8 | ? | ?
4 | 2 | ? | ?
0 | 6 | ? | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
15 | 12 | ? | ?
10 | 8 | ? | ?
4 | 2 | ? | ?
0 | 6 | ? | ?
15 | 12 | 13 | ?
10 | 8 | 9 | ?
4 | 2 | 5 | ?
0 | 6 | 3 | ?
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
15 | 12 | 13 | ?
10 | 8 | 9 | ?
4 | 2 | 5 | ?
0 | 6 | 3 | ?
15 | 12 | 13 | 1
10 | 8 | 9 | 7
4 | 2 | 5 | 11
0 | 6 | 3 | 14
15 | 12 | 13 | 1
10 | 8 | 9 | 7
4 | 2 | 5 | 11
0 | 6 | 3 | 14
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15

## Slide 19: Reversing Shift-Rows: Column Mapping
Idea:
  Fix four bytes
  Check if they map to the same column after Shift-Rows
Observation: Fixing four bytes that map to the same column in Shift-Rows fixes the S-Box accesses at the second round
SHIFT-ROWS
SHIFT-ROWS
MIX-COLUMNS
MIX-COLUMNS

## Slide 20: Column Mapping: Wrong Guess
SHIFT-ROWS
MIX-COLUMNS
First round S-Box accesses of the four fixed plaintext bytes

## Slide 21: Column Mapping: Correct Guess
First round S-Box accesses of the four fixed plaintext bytes
SHIFT-ROWS
MIX-COLUMNS
Second round S-Box accesses of the four fixed plaintext bytes (mapped to the same column at the end of the first round)
Cache accesses here corresponds to the first column of bytes after first round Shift-Rows
ADD-
ROUND-KEY
SUB-BYTES

## Slide 22: Reversing Shift-Rows: Column Ordering
Mix-Columns is a matrix multiplication
2 | 3 | 1 | 1
1 | 2 | 3 | 1
1 | 1 | 2 | 3
3 | 1 | 1 | 2
2 | 3 | 1 | 1
1 | 2 | 3 | 1
1 | 1 | 2 | 3
3 | 1 | 1 | 2
Idea: Fixing three bytes in a column and varying the other results in a predictable behaviour dependent on the varying byte
Result: Knowing how the second round S-Box accesses change as the varying plaintext byte changes identifies its row in the column

## Slide 23: Column Ordering: Example
? |  |  | 
? |  |  | 
? |  |  | 
? |  |  | 
SHIFT-ROWS
MIX-COLUMNS
First round S-Box accesses of the four fixed plaintext bytes
Second round S-Box accesses of the four fixed plaintext bytes
Observe: second round S-Box accesses change when changing the plaintext byte
ADD-
ROUND-KEY
SUB-BYTES

## Slide 24: Column Ordering: Example
11
01
00
00
00
00
00
10
10
10
10
01
01
10
10
11
11
10
10
01
01
00
00
00
00
00
00
11
11
10
10
10
Accesses in first and second S-Boxes are identical up to XOR with constant 102
Varying byte in last row of column
Fixing three bytes and varying the other (in the same column):
There will be two second round S-Box accesses that are identical up to XOR with a constant
Identifying them gives us the row of the varying plaintext byte

## Slide 25: So far …
First Round Attack: gets 2 MSBs of the first round key
Prepared the second round attack by reversing the first round of the key-dependent transformation Shift-Rows

## Slide 26: Second Round Attack
Calculate this.
It will match what we observe in the cache up to a constant.
Guess and
Calculate
It will match what we observe in the cache up to a constant if we guess the correct key.
Observe this in cache
Depends on next
Guess
Calculate
Second round S-Box access
Shift-Rows of first round

## Slide 27: Second Round Attack
For each key byte, guess 6 unknown bits of the first round key and the 8 bits of the second round key
Total possible guesses to test for each key byte
On average, observing S-Box accesses for around different plaintext byte values for each key byte is sufficient

## Slide 28: Summary
Secret-dependent transformations can be reversed by observing cache accesses
To fully break cipher:
  35 million encryptions
  19,472 queries of S-Box accesses
  Average 8 minutes on a typical laptop
Constant-time implementation as a defence for side-channel attacks