## Slide 1
VITI: A Tiny Self-Calibrating Sensor for Power-Variation Measurement in FPGAs
Brian Udugama, Darshana Jayasinghe, Hassaan Saadat,
Aleksandar Ignjatovic, Sri Parameswaran
CHES 2022
September 18-21, 2022
Leuven, Belgium

## Slide 2: This talk is about…
VITI
(voltage induced time
interval sensor)
an area efficient on-chip sensor that
can calibrate itself to measure power
variations on an FPGA.
It can be used for remote power analysis
attacks.
1

## Slide 3: In this talk…
On-chip power sensors
Remote power analysis attacks
Design of VITI
Performance of VITI
2

## Slide 4
On-chip power sensors
&
Remote power analysis
attacks

## Slide 5: On-chip Power Sensors
Measure variations in signal propagation delay
Propagation delay variations are related to changes in operating condition such as supply-voltage
↑ Power consumption leads to
Therefore, signal propagation delay can be used to measure power consumption
Existing on-chip power sensors:
  Time-to-digital converter (TDC)
  Ring oscillator (RO)
  VITI – proposed in this work
  ●●●●
↓ supply-voltage
4

## Slide 6: Remote Power Analysis (RPA) Attacks
Extract cryptographic secrets by analyzing power consumption
Uses on-chip power sensors – no oscilloscopes required
Can be performed remotely without having physical access
“Traditional” Power
Analysis Attacks
Remote Power
Analysis Attacks
5

## Slide 7: Remote Power Analysis (RPA) Attacks
Extract cryptographic secrets by analyzing power consumption
Uses on-chip power sensors – no oscilloscopes required
Can be performed remotely without having physical access
Typical target is an Advanced Encryption Standard (AES) module
A good indication on the sensitivity of an on-chip sensor to small power variations
Key rank (KR)* is used as the performance metric
  KR: the rank of the correct key, when all key guesses are sorted using the information recovered with RPA attack
  Lower the KR, better it is: KR = 1 means, the key is fully recovered
5
* N. Veyrat-Charvillon et al., "Security Evaluations Beyond Computing Power"

## Slide 8: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
6

## Slide 9: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
6

## Slide 10: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
6

## Slide 11: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
6

## Slide 12: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
Requires ≈128 FPGA slices in total
6

## Slide 13: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
Requires ≈128 FPGA slices in total
6

## Slide 14: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
6

## Slide 15: TDC and RO
Sensor | Time-to-digital Converter* | Ring Oscillator+
Placement and routing | Constrained due to long tapped delay line | Arbitrary
Characteristic features | Contains latches Long CARRY chain on floorplan | Contains combinational loops – used in power viruses
Number of sensors | One | Several (≈64)
Resource requirement per sensor | High – 34 FPGA slices | Low – 2 FPGA slices
Sample Alignment | Aligned | Can be misaligned
* F. Schellenberg et al., "An inside job: Remote power analysis attacks on FPGAs"
+ J. Gravellier et al., "High-Speed Ring Oscillator based Sensors for Remote Side-Channel Attacks on FPGAs"
6

## Slide 16
Design of VITI

## Slide 17: Design of VITI
8

## Slide 18: Design of VITI
8

## Slide 19: Design of VITI
Adjustable Input Delay Element
Induced Delay
Tapped Delay Line
8

## Slide 20: Design of VITI
= 1
1
1
1
1
= 1
1
1
1
1
1
Inputs |  | Output
A | B | 
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
Output
8

## Slide 21: Design of VITI
= 1
1
1
1
1
= 1
1
1
1
1
1
Inputs |  | Output
A | B | 
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
Output
8

## Slide 22: Design of VITI
1
= 1
8

## Slide 23: Design of VITI
= 1
1
1
1
1
1
1
0
1
= 1
8

## Slide 24: Design of VITI
Power Consumption
Propagation Delay
Power
Consumption
High
Low
Power
Consumption
1
1
1
0
1
1
1
0
0
9

## Slide 25: Design of VITI
10

## Slide 26: Design of VITI
 Arbitrary placement and routing
 Works with one sensor
 Low resource requirement per sensor
 Aligned samples
 Clock frequency independent resource requirement
 Built-in automatic runtime calibration
11

## Slide 27
RPA Performance of
VITI (4-bit)

## Slide 28: RPA Performance of VITI – Placement of AES module
Varied the placement of AES module
Fixed parameters:
  VITI placement
  VITI frequency – 96 MHz
  Victim AES frequency – 6 MHz
13

## Slide 29: RPA Performance of VITI – Placement of AES module
Can pickup the activity of the victim AES module across the chip
14

## Slide 30: RPA Performance of VITI – Placement of VITI
Varied the placement of VITI
Fixed parameters:
  AES module placement
  VITI frequency – 96 MHz
  Victim AES frequency – 6 MHz
15

## Slide 31: RPA Performance of VITI – Placement of VITI
16

## Slide 32: RPA Performance of VITI – Placement of VITI
16

## Slide 33: RPA Performance of VITI – Placement of VITI
16

## Slide 34: RPA Performance of VITI – Placement of VITI
16

## Slide 35: RPA Performance of VITI – Placement of VITI
16

## Slide 36: RPA Performance of VITI – Placement of VITI
16

## Slide 37: RPA Performance of VITI – Placement of VITI
Placement of VITI has a significant impact on attack efficacy
16

## Slide 38: RPA Performance of VITI – Temperature Change
On-chip sensors are susceptible to temperature changes
Slightly modified CALIBRATION_FSM
Recalibrates when no variation is observed
Fixed parameters:
  VITI/AES module placement
  VITI frequency – 96 MHz
  Victim AES frequency – 6 MHz
While AES module is running, blew hot air over the chip to change the temperature
17

## Slide 39: RPA Performance of VITI – Temperature Change
With recalibration enabled, VITI is capable of adapting to temperature changes
VITI can respond to abrupt changes
18

## Slide 40: RPA Performance of VITI – Resource Efficiency
Sensor | VITI | Time-to-digital Converter | Ring Oscillator
Number of sensors | 1 | 1 | 64
Total sensor area | 8 FPGA slices 2 IODELAY2 elements | 34 FPGA slices | 128 FPGA slices
Block RAM elements for holding samples | 1 | 2 | 64
Size of a power trace with 256 sampling points | 128 bytes | 256 bytes | 16,384 bytes
19

## Slide 41: RPA Performance of VITI – Resource Efficiency
Sensor | VITI | Time-to-digital Converter | Ring Oscillator
Number of sensors |  | 1 | 64
Total sensor area | 8 FPGA slices 2 IODELAY2 elements | 34 FPGA slices | 128 FPGA slices
Block RAM elements for holding samples | 1 | 2 | 64
Size of a power trace with 256 sampling points | 128 bytes | 256 bytes | 16,384 bytes
19

## Slide 42: RPA Performance of VITI – Resource Efficiency
Sensor | VITI | Time-to-digital Converter | Ring Oscillator
Number of sensors |  | 1 | 64
Total sensor area |  | 34 FPGA slices | 128 FPGA slices
Block RAM elements for holding samples | 1 | 2 | 64
Size of a power trace with 256 sampling points | 128 bytes | 256 bytes | 16,384 bytes
19

## Slide 43: RPA Performance of VITI – Resource Efficiency
Sensor | VITI | Time-to-digital Converter | Ring Oscillator
Number of sensors |  | 1 | 64
Total sensor area |  | 34 FPGA slices | 128 FPGA slices
Block RAM elements for holding samples |  | 2 | 64
Size of a power trace with 256 sampling points | 128 bytes | 256 bytes | 16,384 bytes
19

## Slide 44: RPA Performance of VITI – Resource Efficiency
Sensor | VITI | Time-to-digital Converter | Ring Oscillator
Number of sensors |  | 1 | 64
Total sensor area |  | 34 FPGA slices | 128 FPGA slices
Block RAM elements for holding samples |  | 2 | 64
Size of a power trace with 256 sampling points |  | 256 bytes | 16,384 bytes
19

## Slide 45: RPA Performance of VITI
Experimentally evaluated the effects of:
  Frequency of AES module – operating frequency of the victim
  Frequency of VITI – sampling frequency of VITI
  Magnitude of power variation – magnitude of the peak-to-peak variation of the power consumption
Experimentally evaluated the following properties:
  Portability – ability to port VITI across device instances
  Cloud deployability – ability to deploy on a cloud FPGA instance
  Noise tolerance – tolerance to noise due to other active circuits
20

## Slide 46: For more results and information
VITI: A Tiny Self-Calibrating Sensor for Power-Variation Measurement in FPGAs
Udugama, B., Jayasinghe, D., Saadat, H., Ignjatovic, A., & Parameswaran, S.
IACR Transactions on Cryptographic Hardware and Embedded Systems, 2022(1), 657–678.
Artifacts (design sources, sample datasets etc.) are available at https://artifacts.iacr.org/tches/2022/a5/
21

## Slide 47: In this talk…
On-chip power sensors and their characteristics
Remote power analysis (RPA) attacks and key rank (KR)
Design of VITI
Performance and properties of VITI
22

## Slide 48: It is time for your questions!
23

## Slide 49: Thank you! A special thanks to CHES 2022 organizers and sponsors for their generous support for expenses. Thank you!
24