## Slide 1: Triplex: an Efficient and One-Pass Leakage-Resistant Mode of Operation
Yaobin Shen
joint work with Thomas Peters, François-Xavier Standaert,
Gaëtan Cassiers and Corentin Verhamme
UCLouvain Crypto Group
September 19, CHES 2022

## Slide 2: Authenticated Encryption (AE)
Integrity & confidentiality
Protection against side-channel attacks, e.g., masking
KDF
message processing
TGF
tag
KDF
message processing
TGF
tag
significant performance overheads

## Slide 3: How to improve the performance?
Leveled implementation [PSV15]
  avoid equally protecting all parts of an implementation
  identify the protection level of each part (performance gains)
[BPPS17]: DPA-protected KDF/TGF + unbounded leakage for the rest
  substantial performance gains for integrity
[PSV15]: Olivier Pereira, François-Xavier Standaert, Srinivas Vivek: Leakage-Resilient Authentication and Encryption from Symmetric Cryptographic Primitives. CCS 2015: 96-108
[BPPS17]: Francesco Berti, Olivier Pereira, Thomas Peters, François-Xavier Standaert: On Leakage-Resilient Authenticated Encryption with Decryption Leakages. IACR Trans. Symmetric Cryptol. 2017(3): 271-293 (2017)On Leakage-Resilient Authenticated Encryption with Decryption Leakages. IACR Trans. Symmetric Cryptol. 2017(3): 271-293 (2017)
KDF
message processing
TGF
tag
usually the main part

## Slide 4: One-pass Modes: CIML2 + CCAmL1
CIML2 & CCAmL1[BBB+20]
  Ciphertext Integrity with nonce Misuse-resistance and Leakage in enc & dec
  CCA with misuse-resilience and Leakage in enc
Ascon: DPA protection in KGF & TGF [DEMS21]
  sponge-based
[BBB+20]: Bellizia et al.:Spook: Sponge-Based Leakage-Resistant Authenticated Encryption with a Masked Tweakable Block Cipher. IACR Trans. Symmetric Cryptol. 2020(S1): 295-349 (2020)
[DEMS21]: Christoph Dobraunig, Maria Eichlseder, Florian Mendel, Martin Schläffer: Ascon v1.2: Lightweight Authenticated Encryption and Hashing. J. Cryptol. 34(3): 33 (2021)

## Slide 5: One-pass Modes: CIML2 + CCAmL1
TET [BGP+20]
  TBC-based
  rate 1/2 (two TBCs per n-bit message)
[BGP+20]: Francesco Berti, Chun Guo, Olivier Pereira, Thomas Peters, François-Xavier Standaert:TEDT, a Leakage-Resist AEAD Mode for High Physical Security Applications. IACR Trans. Cryptogr. Hardw. Embed. Syst. 2020(1): 256-320 (2020)

## Slide 6: Our Design: Triplex, One-Pass and More Efficient
Triplex: CIML2 + CCAmL1
  rate 2/3 for message (three TBCs per 2n-bit)
  rate 1 for AD (two TBCs per 2n-bit)
TBC with 2n-bit tweak
  Skinny-128-384, Deoxys-TBC-128-384

## Slide 7: Start point: Hirose’s compression function
Hirose’s compression function based on a TBC
  the outputs are random
Encryption rate: 1/2
  two TBCs per n-bit message
1 block for encryption (xor)
1 block used as the subkey for next iteration

## Slide 8: A third TBC call
Rate: 2/3
Authenticity: the tweak is public but influences the outputs
1 block for encryption (xor)
1 block used as the subkey for next iteration
another TBC call for encryption
ciphertext or AD as tweak to be authenticated

## Slide 9: The full-fledged scheme: Triplex
More design considerations
  multi-user security, tag generation [BGPS21],…
encrypt and authenticate messages by Hirose + a third TBC
key derivation function
for 2n-bit initial state
tag generation function
[BGPS21] Francesco Berti, Chun Guo, Thomas Peters, François-Xavier Standaert: Efficient Leakage-Resilient MACs Without Idealized Assumptions. ASIACRYPT (2) 2021: 95-123

## Slide 10: Integrity analysis
bits of CIML2 in the unbounded leakage model
  integrity holds if #queries
requires no protection
DPA protection
DPA protection

## Slide 11: Confidentiality analysis
bits for CCAmL1 due to re-keying process
bits confidentiality without leakage in the nonce misuse-resilient setting [ADL17]
[ADL17] Tomer Ashur, Orr Dunkelman, Atul Luykx: Boosting Authenticated Encryption Robustness with Minimal Modifications. CRYPTO (3) 2017: 3-33

## Slide 12: Comparisons with Other TBC-based LR-AE
Grade 2 = CIML2 + CCAmL1
Grade 3 = CIML2 + CCAmL2
high rate
large

## Slide 13: Implementation results
Triplex-skinny vs Romulus-N
  limited area overhead but significant performance gains
Notes: Triplex and Ascon are levled protected while Romulus-N is uniformly protected.
In Figure A, we show the number of cycles required for encrypting messages of various
length.
1. For short messages, the encryption time is dominated by the KDF and TGF. This
duration is longer for Triplex than for Ascon, mainly due to the larger number of rounds
in Skinny.
2. For longer messages, Ascon takes 24 cycles to encrypt a 64 bit message block,
while Triplex takes 3 × 40 cycles to encrypt 256 bits of message.
3. Overall, Ascon has a slightly better throughput despite a more serial architecture.
But these results are sensitive to the security margins taken by designers.
4. Eventually, the different slope of Romulus-N’s performance confirms an interest of
leveled implementations from the viewpoint of throughput.
In Figure B, we can see that the area of these implementations is dominated by
the masked primitives (confirming the limited overheads of the leveled approach when
high physical security levels are required).
1. So compared to Romulus-N, Triplex has a slightly higher area cost due to the need for both a masked and an unmasked cipher implementations. But this overhead shrinks relatively with a growing number of shares in the masking scheme, and is rewarded with a significantly better performance for messages
larger than 48 bytes.
2. Moreover, we observe that the masked Skinny and Ascon have similar areas for small number of shares, while the area of Ascon grows faster than the one of Skinny.

## Slide 14: Implementation results
Triplex-skinny vs Ascon
  sensitive to security margin: #rounds, #shares
  state size

## Slide 15: Conclusion
Triplex: an efficient and one-pass leakage-resistant AE
  rate 2/3
  bits for CIML2
  bits for standard confidentiality and n/2 bits for CCAmL1
  base on TBC with -bit tweak
Make TBC-based designs more comparable to Sponge-based
Leveled implementation is generally beneficial to improve the performance

## Slide 16
Thanks