## Slide 1
Roulette:
A Diverse Family of Feasible Fault Attacks on Masked Kyber
tii.ae
Jeroen Delvaux Cryptography Research Center
CHES 2022, Leuven, Belgium
Abu Dhabi, UAE

## Slide 2: Our target: Kyber
Post-quantum-secure key encapsulation
Learning with errors
Will be standardized by NIST
ciphertext
Encapsulation:
Decapsulation:
Reject invalid ciphertexts
Decrypt
Hash & Re-encrypt
=?
Hash & KDF
public
symmetric
private
symmetric
Hash & Encrypt
Hash & KDF
random message
constant
Recovered message
02/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
Recovered ciphertext

## Slide 3: Starting point: fault attack from Indocrypt ‘21
Decapsulation:
Decrypt
Hash & Re-encrypt
=?
private
Avalanche effect: either entirely correct or entirely wrong
Depending on the private key, m’1 is either correct or wrong (≈ 50/50)
Bit flip in either input operand of the comparison (using a laser)
Recovered 256-bit message m0 m1 … m255
Recovered ciphertext
Ciphertext polynomial with 4-bit coefficients: v[x] = v0 +
v1 x +
v2 x2 +
…
v255 x255
Bit flip such that v’1 = v1 + 4 mod 16
Success
Failure
m1 = m’1
m1 ≠ m’1
1 linear inequality over the private key (gather 1000s to obtain a solvable system)
03/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute

## Slide 4
We facilitate and diversify the attack
Re-encrypt
=?
Indocrypt ’21:
This work:
Extension of attack surface:
Either input operand of the comparison
Several building blocks of the re-encryption
Relaxed fault model:
Single-bit flips (laser)
Solving inequalities:
≈ 100 minutes
Up to 1% error rate
≤ 1 minute
Up to 25% error rate
Simulation exclusively
ChipWhisperer proof-of-concept
Masking:
Countermeasure
Helps the attack
04/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
Random faults, set-to-0/1 faults, instruction corruption, arbitrary bit-flip patterns, … (various equipment)
(which enables bypassing the IndoCrypt countermeasure)
(which leads to a new countermeasure)

## Slide 5: More faults are needed
 Larger attack surface  More fault models  Masking helps
 More faults (x10… x100)
 Higher execution time (T5): the setup needs to run overnight or during the weekend
Time T = T1 + T2 + T3 + T4 + T5
T1: Training T2: Target preparation (decapsulation, soldering, …)
T3: Building the setup (scripting, …)
T4: Calibration
T5: Execution
 Potential to lower T1 + T2 + T3 + T4 , given that the attacker can use various equipment besides a laser
05/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute

## Slide 6: Larger Attack Surface
Flip 1 bit
=?
v’ = v + 4 mod 16
4
Indocrypt ’21:
This work: rely on fault propagation and multiple attempts
Compress
Barrett reduction
+
x
Centered binomial distribution
Decompress
x
+
-
=?
Fault
Somewhat uniformly distributed on [0, 15]
Somewhat uniformly distributed on [0, 3328]
Analogy: spin a roulette wheel until the ball lands in the desired pocket
Butterflies in the last layer of INTT
06/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
constant
constant
Hash
Hash
Countermeasure bypassed
Countermeasure

## Slide 7: Relaxed Fault Model (and why masking helps)
Flip 1 bit
f
Equipment: laser
f
Example 1:
f2
Example 2: masked hardware
f1
random fault
set-to-{0, 1, constant}
 Unmasked value y is uniform
Example 3: masked software
y1
y2
f2
f1
instruction corruption (or skip)
y
y
x1
y’1 is independent of y1 (or x1)
y2
 Unmasked value y is uniform
Equipment: clock glitching, voltage glitching, EM, laser, …
Indocrypt ’21:
This work:
07/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
x2

## Slide 8: Solving systems of linear inequalities (1/2)
A (public; data from encapsulation)
x
×
≥ 0
< 0
≥ 0
7000 (or more)
1536
∈ [-2, 2]
(decapsulation failure)
(decapsulation success)
b
+
…
…
CBD
Point distributions
…
…
x1
x2
x1536
08/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
First improvement: reduce computation time
In each iteration, compute the distribution of 7000 x 1536 ≈ 10.8 M linear combinations of x1, …, x1536
Indocrypt ’21:
This work:
Exactly (linear convolution): 10.8 M FFTs & IFFTs
Approximate by normal distribution (central limit theorem)
≈ 15 minutes / iteration
≤ 5 seconds / iteration
(single thread)
A (public; data from encapsulation)
x
×
≥ 0
< 0
≥ 0
7000 (or more)
1536
∈ [-2, 2]
(decapsulation failure)
(decapsulation success)
b
+
…
belief propagation (iterative):

## Slide 9: Solving systems of linear inequalities (2/2)
Second improvement: higher error tolerance.
Pr(inequality satisfied | PMF(x)) = Pr(inequality satisfied | PMF(x)) × Pr(inequality correct) + (1 - Pr(inequality satisfied | PMF(x))) × (1 - Pr(inequality correct))
Estimate based on the observed number of decapsulation successes and failures
This work: 25% error rate
Fault injection setup does not need to be perfectly reliable
Importance of CLT-based acceleration increases with the error rate
9/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
Kyber512
Our solver is available on GitHub and as CHES artifact
CHES’21: 1% error rate
Indocrypt’21: 0% error rate

## Slide 10: ChipWhisperer Experiments
First-order masked Kyber768 decapsulation [Coron et al., CHES 2022]
STM32F405 ARM Cortex-M4
Instruction corruption (or skip) in last layer of INTT
Glitching a 24 MHz clock
+
Unfortunately, unoptimized:
Portable C (the NTT is not written in assembly)
24 MHz << 168 MHz
10/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
It would take 5 days to gather enough inequalities for key recovery; we assess their correctness instead

## Slide 11: Concluding Remarks
Our contribution: opening pathways for the attacker
  More building blocks
  More fault models
  Higher error tolerance
  Masking as a facilitator
  More diverse, cheaper, and less reliable fault-injection equipment
Suggestions for further research
  Experiments on an optimized target
  Vulnerability of other PQC algorithms
  Design of new countermeasures
11/11
Roulette: A Diverse Family of Feasible Fault Attacks on Masked Kyber
TII – Technology Innovation Institute
Thank you!

## Slide 12
tii.ae