## Slide 1: A Lightweight Identification Protocol Based on Lattices
Presentation by Thomas Pöppelmann. Joint work with Samed Düzlü, Juliane Krämer, and Patrick Struck of University of Regensburg

## Slide 2: Table of contents
Motivation
1
Our construction
2
Evaluation
3

## Slide 3: The identification problem
Verifier: A party that wants to check the identity of a party
Prover: The party that interacts with the verifier as the asserted party proving its identity
Chips
Practical application:
Prevent counterfeit
Batteries
Machine parts

## Slide 4: Some known solutions in practice
Symmetric keys
Public-key encryption
Digital signatures
EncS(nonce)
nonce
EncPK(nonce)
nonce
nonce
SigSK(nonce)
Verifier
Prover
Prover
Prover
Verifier
Verifier
DecSK(nonce)
DecS(nonce)
SigSK(nonce)

## Slide 5: Practical requirements
Practical requirements towards a post-quantum identification protocol
  Active security
  Protection against physical attacks
  Asymmetric scheme (secret only in Prover)

## Slide 6: Things are different for post-quantum cryptography (PQC)
In Elliptic Curve Crypto signatures and encryption/Diffie-Hellman cost roughly the same and physical protection is well understood
With the new PQC schemes, signatures are getting much more expensive than PKEs/KEMs
Lattice-based PKE/KEM schemes are expensive to protect against side-channel attacks due to properties of the Fujisaki-Okamoto (FO) transform

## Slide 7: Table of contents
Motivation
1
Our construction
2
Evaluation
3

## Slide 8: Starting point: Naïve construction
Instantiation with Kyber requires
FO-transform for active security

## Slide 9: Rationale for FO transform
Goal of the FO transform: Check that the ciphertext was honestly generated
The CPA-secured decryption of Kyber is quite straightforward to protect and relatively fast
But in CCA-secure lattice-based KEMs like Kyber the re-encryption is sensitive to physical attacks
  Re-encryption operates on secret-dependent data
  Re-encryption requires operations that are complex and hard to protect like binomial sampling, hashing, masked comparison, etc.

## Slide 10: Protocol
Our approach
  Move from a 2-pass protocol to a 4-pass protocol
  Prover decrypts a challenge and commits on the response but doesn’t provide it
  Verifier provides randomness used to generate challenge
  Prover re-computes the ciphertext using randomness from Verifier
  If ciphertext was honestly generated the full response is provided and checked

## Slide 11: Table of contents
Motivation
1
Our construction
2
Evaluation
3

## Slide 12: Implementation based on Kyber
Implementation on ARM Cortex-M4 using pq-clean or pqm4 with the m4fspeed variant
Kyber version Kyber768 is used for measurement and comparison later
Caution: We are comparing non-masked vs. x-order masked implementations but this is not sufficient to be secured in practice (e.g., due to fault attacks, template attacks, etc.)

## Slide 13: Results for functional implementation
No difference in cycle counts between our approach and CCA-Kyber as expected (re-encryption is still required)
Signature approach using Dilithium much slower
Implemented using the pqm4 library with m4fspeed.

## Slide 14: Advantage with masking
Protocol becomes more advantageous when increasing the masking order for improves side-channel protection -> Less sensitive code to protect

## Slide 15: Conclusion
We gave an approach to use Kyber in as ID/authentication protocol in a practical setting
Consideration:
  Tradeoff 2-pass vs. 4-pass vs. cost of side-channel hardening?
  Benefit depends on ability of community to improve protection of Kyber against attacks
Thank you for your attention
https://ia.cr/2023/222
See also http://crypt-gen.com/ for GPT-2 based paper abstract generator