## Slide 1: GoFetch: Breaking Constant-Time Cryptographic Implementations Using Data Memory-Dependent Prefetchers
Boru Chen, Yingchen Wang, Pradyumna Shome,
Christopher Fletcher, David Kohlbrenner, Riccardo Paccagnella,
Daniel Genkin
Notes: This talk does not consider the frequency scaling. The type of side-channel we leverage is the cache side channel.
Just have a quick recap.

## Slide 2: Constant-Time Programming
Code
CT Programming
Timing Attacks
Notes: Let’s start with constant-time programming! Constant-time programming is a paradigm to harden the code against timing attacks.

## Slide 3: Constant-Time Programming
Code
CT Programming
Timing Attacks
if (secret) {
...
}
Control-Flow
Load [secret]
Memory Address
DIV secret
Time-Variable
Notes: Constant-time programming is made up of 3 best practices. Namely, the secret data cannot influence control follow, memory access pattern, or be passed as time-variable instruction operands.

## Slide 4: Constant-Time Programming
Code
CT Programming
Timing Attacks
if (secret) {
...
}
Control-Flow
Load [secret]
Memory Address
DIV secret
Time-Variable
secret
Independent
time
Notes: By applying these principles, the program's execution time should be independent of its secret data.

## Slide 5: Constant-Time Programming
Code
CT Programming
Timing Attacks
if (secret) {
...
}
Control-Flow
Load [secret]
Memory Address
DIV secret
Time-Variable
CT Cryptographic
Implementation
secret
Independent
time
Notes: That is, by following these principles, a cryptographic implementation should be free of potential timing attacks.
And cryptographers should be able to have good sleep at night. Sounds Great!

## Slide 6: A Constant-Time Code Example
secret = *non-sec-addr
Notes: All right~ Let’s go through a simple constant-time code example. It is just one-line code that loads a secret value from a non-secret address.

## Slide 7: A Constant-Time Code Example
Memory Address
Control-Flow
Time-Variable
secret = *non-sec-addr
Notes: Since there is no control divergence, no secret-dependent memory access, and no time-variable instruction, it follows all three principles we just mentioned.

## Slide 8: A Constant-Time Code Example
Memory Address
Control-Flow
Time-Variable
Are we safe now?
secret = *non-sec-addr
Notes: So, are we safe now?

## Slide 9: A Constant-Time Code Example
Memory Address
Control-Flow
Time-Variable
Are we safe now?
No!
secret = *non-sec-addr
Notes: Obviously No! That is why I am here today.

## Slide 10: A Constant-Time Code Example
Memory Address
Control-Flow
Time-Variable
Are we safe now?
No!
Apple data memory-dependent prefetcher (DMP) can make a
constant-time code
non-constant-time.
secret = *non-sec-addr
Notes: Our discovery related to data memory-dependent prefetchers, or DMPs, on Apple m-series CPUs shows that this piece of hardware can indeed make constant-time code non-constant-time.

## Slide 11: A Constant-Time Code Example
Memory Address
Control-Flow
Time-Variable
Are we safe now?
No!
Apple data memory-dependent prefetcher (DMP) can make a
constant-time code
non-constant-time.
DMP
Memory Address
secret = *non-sec-addr
Notes: More precisely, we found that the DMP makes this line of code violate the second principle. It makes the memory access pattern secret-dependent.

## Slide 12: A Constant-Time Code Example
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
Notes: The reason is that the DMP can treat any data loaded from memory as an address and perform a memory access to that address.

## Slide 13: A Constant-Time Code Example
Core
Shared Cache
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: For example, let’s say the secret could be one of two distinct pointer values (pointer1 or pointer 2). Suppose they are pointing to different cache lines in the cache.

## Slide 14: A Constant-Time Code Example
Core
Shared Cache
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
*non-sec-addr
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: Without the DMP, no matter what the secret is, there is only one memory access to the non-secret address---which results in the same cache state for both pointer values.

## Slide 15: A Constant-Time Code Example
Core
Shared Cache
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
*non-sec-addr
Core
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: This makes pointer 1 and 2 indistinguishable over timing side channels.

## Slide 16: A Constant-Time Code Example
Core
Shared Cache
DMP
*secret
secret
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
Core
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: With the existence of the DMP, however, the DMP will further perform a memory access to the value returned by the load: the value named secret here.

## Slide 17: A Constant-Time Code Example
Core
Shared Cache
DMP
*ptr1
secret
secret = ptr1
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
Core
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: If the secret equals pointer 1, then pointer 1 will be dereferenced by the DMP.

## Slide 18: A Constant-Time Code Example
Core
Shared Cache
DMP
*ptr2
secret
secret = ptr2
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
Core
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: If the secret is pointer 2, pointer 2 will be dereferenced.

## Slide 19: A Constant-Time Code Example
Core
Shared Cache
DMP
*secret
secret
ptr1
ptr2
Core
Apple DMP could treat loaded data as memory address and perform access.
Memory Address
Control-Flow
Time-Variable
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: Dereferencing pointer 1 or 2 will leave different cache states, which are observable to a co-located attacker. This means that the attacker can tell whether the secret is pointer 1 or 2.

## Slide 20: A Constant-Time Code Example
Apple DMP could treat loaded data as memory address and perform access.
Core
Shared Cache
DMP
Memory Address
Control-Flow
Time-Variable
*secret
secret
Core
ptr1
ptr2
// secret = ptr1 or ptr2
secret = *non-sec-addr
Notes: We conclude that DMP could perform secret-dependent memory access on behalf of the constant-time code and violate the second constant-time principle.
==
This violates the second principle of constant-time programming: the DMP can turn program data into a program address.

## Slide 21: Contribution
Augury1
1 Vicarte, et al., "Augury: Using data memory-dependent prefetchers to leak data at rest”, SP’22.
Notes: You may have heard of Augury before. It was the first work to discover DMPs in Apple M1 chips. But it was not able to demonstrate an actual attack.
We make three contributions over Augury.

## Slide 22: Contribution
Augury1
GoFetch
1 Vicarte, et al., "Augury: Using data memory-dependent prefetchers to leak data at rest”, SP’22.
Comprehensive reverse engineering of Apple DMPs.
Notes: First, through comprehensive reverse engineering, we find that the memory access pattern described in Augury is not necessary to activate the DMP. It was for this reason that Augury could not demonstrate an attack: it's understanding of how the DMP worked made it impractical to exploit.

## Slide 23: Contribution
Augury1
GoFetch
1 Vicarte, et al., "Augury: Using data memory-dependent prefetchers to leak data at rest”, SP’22.
Comprehensive reverse engineering of Apple DMPs.
Develop DMP-aided chosen-input attack framework.
Notes: Second:
With our new-found understanding of when a DMP can activate, we set out to break cryptographic implementations.
We still faced a major hurdle: the DMP is only capable of leaking pointer values.
To overcome this, we developed a new chosen-input attack where the attacker engineers a secret-dependent pointer in intermediate crypto states and exploits the DMP to deduce the secret from it.

## Slide 24: Contribution
Augury1
GoFetch
1 Vicarte, et al., "Augury: Using data memory-dependent prefetchers to leak data at rest”, SP’22.
Comprehensive reverse engineering of Apple DMPs.
Develop DMP-aided chosen-input attack framework.
Undermine four cryptographic implementations in the wild or submitted to NIST PQC standardization.
Notes: Finally, we build end-to-end key extraction attacks to undermine four constant-time cryptographic implementations either deployed in the wild or submitted to NIST PQC standardization. Our attacks range from key exchange to digital signature; from classical to post-quantum cryptography.

## Slide 25: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Memory
Notes: Before we dive into the attack, let's understand the DMP better.
We reverse engineer the DMP and make the following key observations.
First, what is the memory access pattern required to activate the DMP?

## Slide 26: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Memory
ptr
Single memory load
Notes: We find that even a single memory load is enough. Let me say that again: potentially any data loaded from memory is a candidate to be treated as a pointer and dereferenced by the DMP.

## Slide 27: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
L1 Cache
Notes: The next question is where does the DMP scan data to see if it is a pointer?

## Slide 28: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
DMP
L1 Fills
L1 Cache
Notes: We performed experiments to move the pointer value around the memory hierarchy and found that the DMP only monitors L1 cache fills; at which time it scans data in the cache line to see if it looks like a pointer.

## Slide 29: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
DMP
L1 Fills
L1 Cache
How does DMP determine pointers to dereference in each line?
Notes: From this understanding, we further examine how the DMP searches for pointers within a line.

## Slide 30: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
L1 Fills
L1 Cache
How does DMP determine pointers to dereference in each line?
data1
data2
data3
data8
…
DMP
addr
Valid Address?
Notes: It turns out that DMP checks each pointer size-aligned chunk in the line. To successfully dereference a pointer, its target must map to a valid memory region within the process.

## Slide 31: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
L1 Fills
L1 Cache
How does DMP determine pointers to dereference in each line?
data1
data2
data3
data8
…
DMP
addr
Valid Address?
More details in the paper
Notes: More details about DMP’s behaviors are in the paper.

## Slide 32: How to use DMP to break CT Crypto?
Crypto States
01011010010101
Unlike Pointer
Notes: The fact that DMP only leaks pointer value is a significant limitation because crypto states usually look random.
To overcome this issue, we develops a new type of chosen input attack.

## Slide 33: How to use DMP to break CT Crypto?
secret (sec)
chosen input (ci)
intermediate state
(istate)
istate = ci & sec
0xffffffffffffffff
0x0000000000000000
ci & sec
Crypto States
01011010010101
Unlike Pointer
sec
Notes: To see the idea, suppose that our target implementation performs an AND operation between a secret value and an attacker-controlled input.
The secret can be either 64-bit all 0 or all 1, and the attacker's goal is to identify the secret's value.

## Slide 34: How to use DMP to break CT Crypto?
secret (sec)
chosen input (ci)
intermediate state
(istate)
ci & sec
Crypto States
01011010010101
Unlike Pointer
istate = ci & sec
0xffffffffffffffff
0x0000000000000000
sec
Choose ci as valid pointer!
istate = ptr & sec
if sec = 0xffffffffffffffff
=> istate = ptr
if sec = 0x0000000000000000
=> istate = 0
Notes: Now, the attacker says that I am going to use a valid pointer as the input.
If the secret is all 1, the intermediate state will be the pointer. If the secret is all 0, the intermediate state will be masked to 0.

## Slide 35: How to use DMP to break CT Crypto?
secret (sec)
chosen input (ci)
intermediate state
(istate)
Choose ci as valid pointer!
istate = ptr & sec
if sec = 0xffffffffffffffff
=> istate = ptr
if sec = 0x0000000000000000
=> istate = 0
ci & sec
Crypto States
01011010010101
Unlike Pointer
istate = ci & sec
0xffffffffffffffff
0x0000000000000000
sec
DMP
*ptr
DMP
Notes: By monitoring whether the DMP dereferences the pointer, the attacker can infer whether the secret is all 1 or all 0.

## Slide 36: Proof-of-Concept Attacks
Cryptoanalysis for DMP exploit => End-to-end key extraction PoCs
Post-Quantum Cryptography
Classical Cryptography
Key Exchange Scheme
Digital Signature Scheme
OpenSSL DHKE
Go RSA
CRYSTALS-Kyber (ML-KEM)
CRYSTALS-Dilithium (ML-DSA)
OpenSSL DHKE
Go RSA
CRYSTALS-Kyber (ML-KEM)
CRYSTALS-Dilithium (ML-DSA)
Notes: The previous example gives the basic idea. But it assumes just an AND operation between the secret and attacker input. Real crypto implementations are significantly more complex. We perform novel cryptoanalysis and build end-to-end key extraction PoCs for four constant-time cryptographic implementations in the wild.

## Slide 37: Proof-of-Concept Attacks
Cryptoanalysis for DMP exploit => End-to-end key extraction PoCs
Post-Quantum Cryptography
Classical Cryptography
Key Exchange Scheme
Digital Signature Scheme
OpenSSL DHKE
Go RSA
CRYSTALS-Kyber (ML-KEM)
CRYSTALS-Dilithium (ML-DSA)
OpenSSL DHKE
Go RSA
CRYSTALS-Kyber (ML-KEM)
CRYSTALS-Dilithium (ML-DSA)
Notes: To save time, let’s briefly go over ideas for attacking Go’s RSA and CRYSTALS Kyber. Others are detailed in the paper.

## Slide 38: Go RSA
Notes: RSA is a public key encryption scheme. The security of RSA is based on the hardness of factorizing a big public number N. N consists of two prime numbers, p and q. Either recovering p or q is sufficient to break RSA.

## Slide 39: Go RSA
RSA Decryption
Notes: As for the RSA decryption, to decrypt a ciphertext c, c will be raised to secret key d and mod the N.

## Slide 40: Go RSA
CRT Optimization
RSA Decryption
Notes: In Go’s RSA implementation, it adopts Chinese Remainder Theorem optimization to reduce the size of moduli. Instead of computing with modulo N, calculating with modulo p and modulo q separately will be faster.

## Slide 41: Go RSA
CRT Optimization
First Step
RSA Decryption
Notes: Let’s take modulo p part as an example. The first step of the operation is c mod p.

## Slide 42: Go RSA
RSA Decryption
CRT Optimization
Observations of intermediate state :
is chosen input and is secret.
If , then , else .
First Step
Notes: From intermediate states c mod p, we have observations that
c as the ciphertext is the chosen input and p is the secret.
If c less than p, then the output of c mod p remains to be c.
Otherwise, it will subtract several times of p from c.

## Slide 43: Go RSA
Observation of :
is chosen input and is victim’s secret.
if ,
if ,
Target i-th bit of and
set input as !
i-th bit
Notes: From these observations, suppose the attacker has recovered the first i-1 bits of p and says that
I am going to recover the i-th bit of p and craft the input c
Such that it starts with the recovered i-1 bits prefix. And the i-th bit is set as 1. A valid pointer is appended to the end. Other bits are all 0s.

## Slide 44: Go RSA
Observation of :
is chosen input and is victim’s secret.
if ,
if ,
Target i-th bit of and
set input as !
i-th bit
if
  then
if .
  then
Notes: In this case, if the i-th bit of p is 1, then p will be greater than c with overwhelming probability. And c mod p will still be c and contain the pointer.
If the i-th bit of p is 0, then p will definitely be less than c. And because of the reduction by several times of p, the pointer in c is likely to be tampered. And there will be no pointer in c mod p.
As a result, by monitoring whether the DMP dereferences the pointer, the attacker learns the i-th bit of p.

## Slide 45: Go RSA
DMP recovers upper 560 bits
+ Coppersmith2
= full extraction!
2 Coppersmith, ”Finding a small root of a bivariate integer equation; factoring with high bits known”, EUROCRYPT’96.
Observation of :
is chosen input and is victim’s secret.
if ,
if ,
Target i-th bit of and
set input as !
i-th bit
Notes: Similar strategy can be used to target other bits of p.
For RSA-2048, we leverage the DMP to recover upper 560 bits of the secret prime. Also, since the attacker knows more than half of higher order bits of the secret prime, it can use Coppersmith algorithm to fully extract the whole prime and thus break the RSA.

## Slide 46: CRYSTALS-Kyber (ML-KEM)
CCA-KEM built on a CPA-PKE scheme.
Notes: Let’s move on to our post-quantum crypto example, Kyber. Kyber is a chosen cipher attack secure key encapsulation mechanism that is built on a chosen plaintext attack secure public key encryption scheme.

## Slide 47: CRYSTALS-Kyber (ML-KEM)
CCA-KEM built on a CPA-PKE scheme.
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: Prior literature has studied the key mismatch attack targeting the inside PKE scheme. Our attack gets inspiration from it.

## Slide 48: CRYSTALS-Kyber (ML-KEM)
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Key Mismatch Attack3
Notes: To quickly catch the point of this attack, let’s go over the key components of the inside PKE scheme and bear in mind the key observations with regard to them,
On the encryption function side, there are three inputs, the original message (or plaintext) m, the public key pk and an error term e.

## Slide 49: CRYSTALS-Kyber (ML-KEM)
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Key Mismatch Attack3
…
Notes: The original message m is a vector of a 1-bit value, which means that each index of m is either 0 or 1.

## Slide 50: CRYSTALS-Kyber (ML-KEM)
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Key Mismatch Attack3
…
…
Kyber-512:
Notes: The error e is a vector of integer that has the same length as m. Each element of e ranges from 0 to q. Here, q is a public constant. In Kyber-512, q equals to 3329.

## Slide 51: CRYSTALS-Kyber (ML-KEM)
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Key Mismatch Attack3
…
…
Kyber-512:
chosen
inputs
Notes: Since the encryption function is performed by the attacker, the attacker has control over the original message m and the error e.

## Slide 52: CRYSTALS-Kyber (ML-KEM)
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Key Mismatch Attack3
…
…
Kyber-512:
chosen
inputs
secret
Notes: The encryption function then outputs the ciphertext c and passes it to the decryption function.
The decryption function processes the ciphertext with the secret key sk and generates the decrypted message m’.

## Slide 53: CRYSTALS-Kyber (ML-KEM)
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Key Mismatch Attack3
…
…
Kyber-512:
chosen
inputs
secret
Notes: Ideally, as a correct PKE scheme, we want the decrypted message m’ equals to the original message. However, for some special combination of the error term and secret key, mismatch between m and m’ could happen.

## Slide 54: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: The key observation is that
there exists a one to one relationship between each index of the decrypted message and the original message.
For index i, if sk is less than q/4 – e, then m’ equals to m, no mismatch, cool
if sk is greater than or equals q/4 – e, then m’ does not equal m. In other words, this index of the message flips.
Since the attacker can tweak the error e, if it knows whether the mismatch happens, it can adaptively collect inequations and recover sk index by index.

## Slide 55: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
FO transformation wraps CPA to CCA.
Kyber PKE
Kyber
FO
Observations of decrypted message :
is secret, and are chosen inputs.
if ,
if ,
Notes: To fight against the mismatch attack, Kyber wraps the CPA PKE scheme with the FO transformation. This transformation prevents the mismatch information from kyber’s output.

## Slide 56: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
FO transformation wraps CPA to CCA.
Kyber PKE
Kyber
FO
DMP
Observations of decrypted message :
is secret, and are chosen inputs.
if ,
if ,
Notes: However, as we know, the DMP can bypass it and examine the intermediate state m’.

## Slide 57: CRYSTALS-Kyber
Set as and tweak !
if
  then
if
  then
No
Observations of decrypted message :
is secret, and are chosen inputs.
if ,
if ,
Notes: To leak the first coefficient of s, the attacker starts m with a pointer and fills others with 0. Based on prior observations,
if the first coefficient of e+s is less than q over 4, than no bit flip and pointer remains in m’.
If it is greater than q over 4, then first bit of pointer will be flipped. And m’ does not have the pointer.
By monitoring DMP dereference to the pointer, the attacker will know which one is the case and collect inequations, just like the key mismatch attack.

## Slide 58: CRYSTALS-Kyber
Set as and tweak !
3 May et al., ”Too Many Hints – When LLL Breaks LWE”, ASIACRYPT’23.
DMP recovers 392 coefficients
+ Lattice Reduction3
= full extraction!
if
  then
if
  then
No
Kyber-512:
Observations of decrypted message :
is secret, and are chosen inputs.
if ,
if ,
Notes: Similar strategy could be used to leak other coefficients of s.
For Kyber-512, we leverage DMP to leak 392 coefficients among 512. And we further run the latest lattice reduction tool to uncover other coefficients.

## Slide 59: Mitigations
*istate
Core
Shared Cache
DMP
istate
Core
Notes: From above real crypto examples, we have better understanding of how DMP gets involved in the chosen input attack.
But how do we protect ourselves from the DMP. Here are three intuitive ideas.
First, we can just turn off the DMP.
Although we don’t know how to do this on M1 and M2 chips, setting a data independent timing bit on M3 can effectively disable the DMP.
Second, the DMP only reacts on pointer values. Crypto implementations can apply random mask to critical crypto states.
Finally, we can use more restrictive scheduling policy to avoid co-location, so that the attacker cannot observe the DMP’s activity.

## Slide 60: Mitigations
Core
Shared Cache
DMP
istate
Core
Set Data Independent Timing Bit
Only M3 processor!
Disable DMP
Notes: From above real crypto examples, we have better understanding of how DMP involved in the chosen input attack.
But how do we protect ourselves from the DMP. Here are three intuitive ideas.
First, we can just turn off the DMP.
Although we don’t know how to do this on M1 and M2 chips, setting a data independent timing bit on M3 can effectively disable the DMP.
Second, the DMP only reacts on pointer values. Crypto implementations can apply random mask to critical crypto states.
Finally, we can use more restrictive scheduling policy to avoid co-location, so that the attacker cannot observe the DMP’s activity.

## Slide 61: Mitigations
Core
Shared Cache
DMP
*(istate⊕rand)
istate⊕rand
Core
istate⊕rand
ptr
Disable DMP
Blinding
Notes: From above real crypto examples, we have better understanding of how DMP involved in the chosen input attack.
But how do we protect ourselves from the DMP. Here are three intuitive ideas.
First, we can just turn off the DMP.
Although we don’t know how to do this on M1 and M2 chips, setting a data independent timing bit on M3 can effectively disable the DMP.
Second, the DMP only reacts on pointer values. Crypto implementations can apply random mask to critical crypto states.
Finally, we can use more restrictive scheduling policy to avoid co-location, so that the attacker cannot observe the DMP’s activity.

## Slide 62: Mitigations
Core
Shared Cache
DMP
*istate
istate
Core
Disable DMP
Blinding
Prevent co-location
Notes: From above real crypto examples, we have better understanding of how DMP involved in the chosen input attack.
But how do we protect ourselves from the DMP. Here are three intuitive ideas.
First, we can just turn off the DMP.
Although we don’t know how to do this on M1 and M2 chips, setting a data independent timing bit on M3 can effectively disable the DMP.
Second, the DMP only reacts on pointer values. Crypto implementations can apply random mask to critical crypto states.
Finally, we can use more restrictive scheduling policy to avoid co-location, so that the attacker cannot observe the DMP’s activity.

## Slide 63: Conclusion
gofetch.fail
Check our Website:
boruc2@illinois.edu
Data memory-dependent prefetchers (DMPs) put any pointers-like secret data at risk.
Exploiting DMPs to perform key extraction attacks to constant-time cryptography is feasible.
Notes: Thank you all~ I can take questions now.

## Slide 64: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Notes: To understand this attack, we can simplify the process of encryption and decryption as follows.
First, before going into the encryption function, the input bit-string plaintext, or original message m is converted to a polynomial form mp.

## Slide 65: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Notes: To understand this attack, we can simplify the process of encryption and decryption as follows.
First, before going into the encryption function, the input bit-string plaintext, or original message m is converted to a polynomial form mp.

## Slide 66: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Notes: To convert a single bit of m to a coefficient of mp, Kyber maps the value1 to the coefficient q/2, and maps value 0 to coefficient 0.

## Slide 67: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Notes: And then mp will go over both encryption and decryption function.
The output of decryption function is mp’. mp’ equals to mp plus an error term, capital E.

## Slide 68: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Decrypted
Notes: Finally, polynomial mp’ is converted to the decrypted message m’.
For each coefficient of mp’, if it is between q/4 and 3q/4, in other words, it points to the orange region, then it is converted to value 1 in m. If it points to the green region, then it is converted to value 0 in m.

## Slide 69: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Decrypted
Notes: Mismatch happens when the error, capital E is too big that it makes corresponding coefficients of mp and mp’ point to different region

## Slide 70: CRYSTALS-Kyber
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Original
Decrypted
Bit Flip!!
Notes: As a result, we can see one bit flip between original message m and decrypted message m’.

## Slide 71: CRYSTALS-Kyber
secret
chosen input
Bold symbol refers to vector of polynomial.
Observations of decrypted message :
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: If we take a closer look at the capital E, we will find that it consists of secret s and other chosen input terms.

## Slide 72: CRYSTALS-Kyber
secret
chosen input
secret
chosen input
Simplify
Bold symbol refers to vector of polynomial.
Observations of decrypted message :
is secret, is chosen input.
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: Since the attacker can control the chosen input part, this expression can be simplified as e2 + s. e2 is the chosen input and s is the secret.

## Slide 73: CRYSTALS-Kyber
Observations of decrypted message :
is secret, is chosen input.
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: And then we can have a clear picture of the mapping from mp’ to the decrypted plaintext m’.
Let’s say one bit of plaintext m is 1, then the corresponding coefficient mp would be q over 2.

## Slide 74: CRYSTALS-Kyber
Observations of decrypted message :
is secret, is chosen input.
if ,
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: mp’ is the sum of mp, e2 and s. if e2+s is less than q / 4, mp’ will still point to orange region, which says corresponding bit of m’ is 1, the same as m. So no mismatch. Cool

## Slide 75: CRYSTALS-Kyber
Observations of decrypted message :
is secret, is chosen input.
if ,
if ,
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: if e2+s is greater or equal q / 4, mp’ will point to green region, which says corresponding bit of m’ is 0. Oops! Bit flip and mismatch happens.

## Slide 76: CRYSTALS-Kyber
Observations of decrypted message :
is secret, is chosen input.
if ,
if ,
Key Mismatch Attack3
3 Qin et al., ”A Systematic Approach and Analysis of Key Mismatch Attacks on Lattice-Based NIST Candidate KEMs”, ASIACRYPT’21.
Notes: With the knowledge of whether mismatch happens for a certain bit, we can construct inequations with regard to corresponding coefficient of secret s.
We can further tweak e2 to get more inequations, and finalize the value of the secret s.

## Slide 77: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
Notes: To understand this attack, we only need to focus on the construction of the decryption function. Variables here are polynomials.
m is plaintext and m’ is the output of the decryption, which may not equal to m when mismatch happens.
The output of the decryption function could be interpreted as XOR plaintext m with a mask.
This mask comes from scaling down and rounding each coefficient of capital E to either 0 or 1.

## Slide 78: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
secret
chosen input
Observations of decrypted plaintext :
Bold symbol refers to vector of polynomial.
Notes: If we take a closer look at the capital E, we will find that s is the secret and other components are all chosen inputs.

## Slide 79: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
secret
chosen input
Observations of decrypted plaintext :
Bold symbol refers to vector of polynomial.
Notes: If we take a closer look at the capital E, we will find that s is the secret and other components are all chosen inputs.

## Slide 80: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
secret
chosen input
Observations of decrypted plaintext :
is secret, is chosen input.
Notes: Since the attacker can tweak all the chosen inputs, we can simplify the expression as e2 + s, where e2 is the chosen input and the s is the secret.

## Slide 81: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
1
0
0
…
0
0
0
…
1
0
0
…
Observations of decrypted plaintext :
is secret, is chosen input.
if ,
.
Notes: Now we can visualize the XOR operation and see when the mismatch takes place.
For one coefficient, if e2 + s is less than q over 4, then the mask will be 0, and m will equal m’. No mismatch happens.

## Slide 82: CRYSTALS-Kyber
CCA-KEM built on a CPA-PKE scheme.
Observations of decrypted plaintext :
is secret, is chosen input.
if ,
.
if ,
.
Bit Flip!!
1
0
0
…
0
0
0
…
1
0
0
…
Notes: If e2 + s is greater or equal to q over 4, then the mask will be 1. A bit mismatch or flip happens between m and m’.
If the attacker could get m and m’ or whether there is a bit flip, then it can construct an inequation regarding the secret s.
With multiple inequations, the secret s could be recovered.

## Slide 83: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
L1 Fills
L1 Cache
How does DMP determine pointers to dereference in each line?
data1
data2
data3
data8
…
DMP
addr
=
data2
addr
Notes: For each chunk, the DMP adopts a heuristic filter that only considers the pointer value having the same upper 32-bit prefix as the virtual address where it is located.

## Slide 84: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
L1 Fills
L1 Cache
How does DMP determine pointers to dereference in each line?
data1
data2
data3
data8
…
DMP
addr
=
data2
addr
Valid Address!
Notes: Meanwhile, to successfully perform the pointer dereferences, the target must map to a valid memory region within the process.

## Slide 85: Key Observations of Apple DMP
Core
What is the memory access pattern required?
Where does the DMP scan for pointers?
data
L1 Fills
L1 Cache
How does DMP determine pointers to dereference in each line?
data1
data2
data3
data8
…
DMP
addr
=
data2
addr
Valid Address!
More details in the paper
Notes: More details about DMP’s behaviors are in the paper.

## Slide 86: Constant-Time Programming
A paradigm to harden the code against side-channel.
Duration of execution does not depend on the secret.
Notes: Let’s start with the constant-time programming! Constant-time programming is a paradigm to harden the code against side-channel attack. Basically, it means that any secret information doesn’t influence the usage of the hardware resource and how long a bunch of instructions take.
Since such a golden rule is too abstract to follow, we have three best practices it implies.
That is. Secret data cannot determine the control follow, cannot pass to time-variable instruction operands, cannot decide the memory address to access.
All of them are subject to timing attack or cache attacks.

## Slide 87: Constant-Time Programming
A paradigm to harden the code against side-channel.
Duration of execution and hardware usage do not depend on the secret.
if (secret) {
...
}
Control-Flow
Notes: Let’s start with the constant-time programming! Constant-time programming is a paradigm to harden the code against side-channel attack. Basically, it means that any secret information doesn’t influence the usage of the hardware resource and how long a bunch of instructions take.
Since such a golden rule is too abstract to follow, we have three best practices it implies.
That is. Secret data cannot determine the control follow, cannot pass to time-variable instruction operands, cannot decide the memory address to access.
All of them are subject to timing attack or cache attacks.

## Slide 88: Constant-Time Programming
A paradigm to harden the code against side-channel.
Duration of execution and hardware usage do not depend on the secret.
if (secret) {
...
}
DIV secret
Control-Flow
Time-Variable Instruction
Notes: Let’s start with the constant-time programming! Constant-time programming is a paradigm to harden the code against side-channel attack. Basically, it means that any secret information doesn’t influence the usage of the hardware resource and how long a bunch of instructions take.
Since such a golden rule is too abstract to follow, we have three best practices it implies.
That is. Secret data cannot determine the control follow, cannot pass to time-variable instruction operands, cannot decide the memory address to access.
All of them are subject to timing attack or cache attacks.

## Slide 89: Cache attacks
What is a cache?
  A layer to reduce memory access latency.
Core
Cache
DRAM
Notes: Firstly, let's do a quick recap of cache attacks.
So, what is a cache?
A cache is a layer between CPU cores and main memory aimed at reducing memory access latency.

## Slide 90: Cache attacks
Core
Cache
DRAM
What is a cache?
  A layer to reduce memory access latency.
Cache miss costs longer time than cache hit.
Notes: When a core tries to load a data, if the data is in the cache, then it will be fast to retrieve; Otherwise, we need to get to the DRAM to fetch the data, which costs longer time.

## Slide 91: Cache attacks
Core
Core
Shared Cache
What is a cache?
  A layer to reduce memory access latency.
Cache miss costs longer time than cache hit.
Cache is shared by multi-processes or even multi-cores.
Notes: Typically, a cache is shared by multi-processes on the same core, or even across cores.

## Slide 92: Cache attacks
Core
Core
Shared Cache
set 0
set i
set n
…
…
What is a cache?
  A layer to reduce memory access latency.
Cache miss costs longer time than cache hit.
Cache is shared by multi-processes or even multi-cores.
Set-associative cache.
Notes: Cache is usually organized in a set-associative manner, where the set id is determined by a certain part of the memory address and when all the ways/columns in the target set are occupied by other cache lines, one of them will be replaced by the new line.

## Slide 93: Cache attacks
Core
Core
Load sec [sec_addr]
…
Load y [sec]
Shared Cache
set 0
set i
set n
…
…
Notes: Let's see a victim's code snippet. First, it loads the secret sec from the memory. And later, it treats the sec as a memory address to perform a data load.

## Slide 94: Cache attacks
Core
Core
Load sec [sec_addr]
…
Load y [sec]
Shared Cache
set 0
set i
set n
…
…
Notes: To learn the sec, before victim's second load, the attacker loads bunch of data to prime the whole cache.

## Slide 95
Core
Core
Load sec [sec_addr]
…
Load y [sec]
Shared Cache
set 0
set i
set n
…
…
Cache attacks
Notes: And then, victim loads address sec, which replaces one block in set i.

## Slide 96: Cache attacks
Core
Core
Load sec [sec_addr]
…
Load y [sec]
Shared Cache
Miss
Hit
Hit
Hit
set 0
set i
set n
…
…
Notes: Finally, the attacker re-accesses all the data it has loaded and measures their access latency. Apparently, when it goes through set i, one of lines will need longer time to get back.

## Slide 97: Cache attacks
Core
Core
Load sec [sec_addr]
…
Load y [sec]
Shared Cache
Miss
Hit
Hit
Hit
set 0
set i
set n
…
…
sec leaks!
Notes: According to the set number, the attacker can learn partial information of sec.

## Slide 98: No!
Core
Core
Load sec [sec_addr]
…
Load y [sec]
Shared Cache
set 0
set i
set n
…
…
We found that data memory-dependent prefetcher (DMP) on Apple M-series CPU could treat data as memory address and perform access.
sec
DMP
pointer or not?
Notes: Obviously, the answer is NO. That is why I am here today.
Our new discovery toward data memory-dependent prefetcher or DMP on Apple m-series CPUs shows that the DMP could treat data as memory address and perform the access on the behalf of the program.
When the victim loads sec from the memory, the DMP will scan sec and think about whether it is a pointer or not.

## Slide 99: No!
Load sec [sec_addr]
Load [sec]
…
Load y [sec]
sec
DMP
*sec
Core
Core
Shared Cache
Miss
Hit
Hit
Hit
set 0
set i
set n
…
…
sec leaks!
We found that data memory-dependent prefetcher (DMP) on Apple M-series CPU could treat data as memory address and perform access.
Notes: If it believes that it is a pointer, then it will dereference it. Just like insert a load instruction in the code. The sec is leaked again!

## Slide 100: No!
Load sec [sec_addr]
Load [sec]
…
Load y [sec]
sec
DMP
*sec
Core
Core
Shared Cache
Miss
Hit
Hit
Hit
set 0
set i
set n
…
…
sec leaks!
DMP does not understand the program semantic and puts any data
brought from the memory
looks like pointer
at risk.
Notes: We need to point out that DMP does not understand the actual usage of sec. It might just a normal data brought from the memory, but looks like pointer. Its appearance induces the DMP to leak it.

## Slide 101: A Constant-Time Code Example
Memory Address
Load secret[non-sec-addr]
Apple DMP could treat data as memory address and perform access.
Notes: Obviously No! Hardware is usually unfriendly and implicitly violates the rules. That is why I am here today.
Our new discovery toward data memory-dependent prefetcher or DMP on Apple m-series CPUs shows that the DMP could treat data as memory address and perform the access on the behalf of the program.
When the victim loads sec from the memory, the DMP will scan sec and think about whether it is a pointer or not. If it believes that it is a pointer, then it will dereference it. Just like insert a load instruction in the code. This load operation would leave a secret dependent trace in the cache. And cache state is observable to a co-location attacker through traditional cache side-channels.
We need to point out that DMP does not understand the actual usage of sec. It might just a normal data brought from the memory, but look like pointer. Its appearance induces the DMP to leak it.
You may have heard Augury before. It was the first work discovering DMP in Apple M1 chips. However, it has a totally different DMP activation model and underestimates the leakage of the DMP.

## Slide 102: A Constant-Time Code Example
Apple DMP could treat data as memory address and perform access.
secret
DMP
Pointer?
Core
Shared Cache
Memory Address
Load secret[non-sec-addr]
Notes: Obviously No! Hardware is usually unfriendly and implicitly violates the rules. That is why I am here today.
Our new discovery toward data memory-dependent prefetcher or DMP on Apple m-series CPUs shows that the DMP could treat data as memory address and perform the access on the behalf of the program.
When the victim loads sec from the memory, the DMP will scan sec and think about whether it is a pointer or not. If it believes that it is a pointer, then it will dereference it. Just like insert a load instruction in the code. This load operation would leave a secret dependent trace in the cache. And cache state is observable to a co-location attacker through traditional cache side-channels.
We need to point out that DMP does not understand the actual usage of sec. It might just a normal data brought from the memory, but look like pointer. Its appearance induces the DMP to leak it.
You may have heard Augury before. It was the first work discovering DMP in Apple M1 chips. However, it has a totally different DMP activation model and underestimates the leakage of the DMP.

## Slide 103: A Constant-Time Code Example
Apple DMP could treat data as memory address and perform access.
secret
Core
Shared Cache
Memory Address
Load secret[non-sec-addr]
*secret
DMP
Notes: Obviously No! Hardware is usually unfriendly and implicitly violates the rules. That is why I am here today.
Our new discovery toward data memory-dependent prefetcher or DMP on Apple m-series CPUs shows that the DMP could treat data as memory address and perform the access on the behalf of the program.
When the victim loads sec from the memory, the DMP will scan sec and think about whether it is a pointer or not. If it believes that it is a pointer, then it will dereference it. Just like insert a load instruction in the code. This load operation would leave a secret dependent trace in the cache. And cache state is observable to a co-location attacker through traditional cache side-channels.
We need to point out that DMP does not understand the actual usage of sec. It might just a normal data brought from the memory, but look like pointer. Its appearance induces the DMP to leak it.
You may have heard Augury before. It was the first work discovering DMP in Apple M1 chips. However, it has a totally different DMP activation model and underestimates the leakage of the DMP.

## Slide 104: A Constant-Time Code Example
Apple DMP could treat data as memory address and perform access.
secret
Core
Shared Cache
Memory Address
Load secret[non-sec-addr]
Load [secret] // DMP ACCESS
DMP
*secret
Notes: Obviously No! Hardware is usually unfriendly and implicitly violates the rules. That is why I am here today.
Our new discovery toward data memory-dependent prefetcher or DMP on Apple m-series CPUs shows that the DMP could treat data as memory address and perform the access on the behalf of the program.
When the victim loads sec from the memory, the DMP will scan sec and think about whether it is a pointer or not. If it believes that it is a pointer, then it will dereference it. Just like insert a load instruction in the code. This load operation would leave a secret dependent trace in the cache. And cache state is observable to a co-location attacker through traditional cache side-channels.
We need to point out that DMP does not understand the actual usage of sec. It might just a normal data brought from the memory, but look like pointer. Its appearance induces the DMP to leak it.
You may have heard Augury before. It was the first work discovering DMP in Apple M1 chips. However, it has a totally different DMP activation model and underestimates the leakage of the DMP.

## Slide 105: A Constant-Time Code Example
Apple DMP could treat loaded data as memory address and perform access.
Core
Shared Cache
Memory Address
// secret = ptr1 or ptr2
Load secret[non-sec-addr]
Core
DMP
Augury1
GoFetch
1 Vicarte, et al., "Augury: Using data memory-dependent prefetchers to leak data at rest," SP’22.
ptr1
ptr2
secret
*secret
Notes: All right~ Let’s go through a simple constant-time code example. Just a one-line code.
A secret value is loaded from a non-secret address.
Since there is no control divergence, no secret-dependent memory address, and no time-variable operation, it follows all three principles we just mentioned.
So, are we safe now?
Obviously No! That is why I am here today.
Our discovery towards data memory-dependent prefetcher or DMP on Apple m-series CPUs shows that this piece of hardware could make a constant-time code non-constant-time. To be precise, we find that DMP will make this line of code violate the second principle, secret-dependent memory access.
The reason is that the DMP could treat any data loaded from the memory as an address and perform memory access.
For example, let’s say the secret could be one of distinct pointer values (pointer1 or pointer 2).
When the secret is loaded from the memory, the DMP will activate for potential pointer value and dereference it. If the secret equals pointer 1, then pointer 1 will be dereferenced; otherwise, pointer 2 will be dereferenced. Dereferencing different pointers will leave different cache states, which are observable by a co-location attacker. Therefore, the attacker can tell whether the secret is pointer 1 or 2.
You may have heard Augury before. It was the first work discovering DMP in Apple M1 chips. However, it has a different view of DMP activation and underestimates the leakage of the DMP.

## Slide 106: Data Memory-Dependent Prefetcher (DMP)
A class of Hardware Prefetcher
  Fetch data used in the future
  E.g. Stride Prefetcher
for (i = 0; i < N; i++)
arr[i];
arr[0]
arr[1]
arr[2]
arr[N-1]
…
arr[N]
arr[M-1]
…
Training
Prefetching
Notes: Before we dive into the attack, let's understand the DMP better.

## Slide 107: Data Memory-Dependent Prefetcher (DMP)
A class of Hardware Prefetcher
  Fetch data used in the future
  E.g. Stride Prefetcher
DMP deals with irregular access pattern directed by content
  E.g. Add a de-reference operator on arr[i]
for (i = 0; i < N; i++)
*arr[i];
arr[0]
arr[1]
arr[2]
arr[N-1]
…
arr[N]
*
*
*
*
*
arr[M-1]
*
…
Training
Prefetching

## Slide 108: Apple DMP – No training required
arr[0]
arr
arr[1]
arr[2]
arr[7]
…
Data_Buf
0
1
2
7
// arr fits in a cache line
uint64_t arr[8];
// fill arr[8] with test
addresses
FLUSH_CACHE();
tmp += arr[0];
// measure access latency to
test addresses

## Slide 109: Apple DMP – No training required
arr[0]
arr
arr[1]
arr[2]
arr[7]
…
Data_Buf
0
1
2
7
Load
// arr fits in a cache line
uint64_t arr[8];
// fill arr[8] with test
addresses
FLUSH_CACHE();
tmp += arr[0];
// measure access latency to
test addresses

## Slide 110: Apple DMP – No training required
arr[0]
arr
arr[1]
arr[2]
arr[7]
…
Data_Buf
0
1
2
7
Load
// arr fits in a cache line
uint64_t arr[8];
// fill arr[8] with random
numbers
FLUSH_CACHE();
tmp += arr[0];
// measure access latency to
test addresses

## Slide 111: Apple DMP – No training required
// arr fits in a cache line
uint64_t arr[8];
// fill arr[8] with test
addresses/random numbers
FLUSH_CACHE();
tmp += arr[0];
// measure access latency to
test addresses

## Slide 112: Apple DMP-Aided Chosen-Input Attack
Attacker-controlled input:
Victim secret:
Core
…
…
L1 Cache

## Slide 113: Apple DMP-Aided Chosen-Input Attack
Attacker-controlled input:
Victim secret:
Intermediate value:
Core
…
…
L1 Cache

## Slide 114: Apple DMP-Aided Chosen-Input Attack
Attacker-controlled input:
Victim secret:
Intermediate value:
Core
…
…
L1 Cache
Evict

## Slide 115: Apple DMP-Aided Chosen-Input Attack
Attacker-controlled input:
Victim secret:
Intermediate value:
Core
…
…
L1 Cache
DMP
L1 Fills

## Slide 116: Apple DMP-Aided Chosen-Input Attack
Attacker-controlled input:
Victim secret:
Intermediate value:
Attacker predicate: , where
Core
…
…
L1 Cache
DMP
L1 Fills
*
?
More details in the paper

## Slide 117: RSA-2048
0···0
recovered prefix
1
0···0
0···0
ptrs
1024
n-1
560-n
16
448
n-th
0···0
recovered prefix
?
To be leaked
Trailing
=

## Slide 118: OpenSSL Diffie-Hellman
Window-based exponentiation algorithm

## Slide 119: CRYSTALS-Dilithium

## Slide 120: GoFetch: Breaking Constant-Time Cryptographic Implementations Using Data Memory-Dependent Prefetchers
Boru Chen, Yingchen Wang, Pradyumna Shome,
Christopher Fletcher, David Kohlbrenner, Riccardo Paccagnella,
Daniel Genkin