## Slide 1: Stealing Cryptographic Keys with Weird Gates
Chitchanok Eyal Yuval
Chuengsatiansup Ronen Yarom

## Slide 2: Publications
The Gates of Time: Improving Cache Attacks with Transient Execution [Usenix 23]
Daniel Katzman
William Kosasih
Chitchanok Chuengsatiansup
Eyal Ronen
Yuval Yarom
Spec-o-Scope: Cache Probing at Cache Speed [CCS 24]
Gal Horowitz
Eyal Ronen
Yuval Yarom

## Slide 3: Outline of the talk
Weird gates on microarchitectural state
  Definition of the logical state of cache
  Computing on the logical state with weird gates
Exploiting weird gates for fun and profit
  Computation with weird gates
  Weird gates Vs Coarse grain timers
  Weird gates Vs S-Box based AES implementations

## Slide 4: Logical State of the Microarchitectural Cache
F F F T F F F F T F F F F
Associate a logical Boolean value with each memory addresses
  TRUE – address is cached
  FALSE – address is not cached
Flushing sets a value to FALSE
Accessing memory sets a value to TRUE (may also set another to FALSE)
Measuring access time observes value (and set to TRUE)
What else?
Processor
Memory
Cache
F
T

## Slide 5: Conditional access
What is the cache state of *out after execution?
TRUE if *in != 0.
What if *in == 0?
if (*in == 0)
return;
out += 0;
out += 0;
a = *out
Assume *in == 0

## Slide 6: Speculative execution
if (*in == 0)
return;
out += 0;
out += 0;
a = *out
Evaluation of branch conditions can take time
The CPU predicts future execution
  Correct prediction – win
  Incorrect prediction – rollback
  Microarchitectural state remains
May be executed even if *in == 0
Assume
*in == 0
Assume branch mispredicted

## Slide 7: Conditional Speculative Execution
Assume
*in == 0
Branch mispredicted
if (*in == 0)
return;
out += 0;
out += 0;
a = *out
Load *in
Load *out
branch
*in cached
*in not cached
Load *in
Load *out
branch
Delay
Delay

## Slide 8: Weird NOT gate
Assume
*in == 0
Branch mispredicted
if (*in == 0)
return;
out += 0;
out += 0;
a = *out
Load *in
Delay
Load *out
branch
Load *in
Delay
Load *out
branch
*in cached
*in not cached
*in | *out
TRUE | FALSE
FALSE | TRUE
out  NOT(in)

## Slide 9: Thinking about this
Chains
Load *in
Delay
Load *out
branch
Signal
Probe
Control
Delay

## Slide 10: Combining Chains
if (*in1 + *in2 == 0)
return;
out += 0
a = *out
Load *in1
Load *in2
Delay
Load *out
branch
*in1 | *in2 | *out
FALSE | FALSE | TRUE
FALSE | TRUE | TRUE
TRUE | FALSE | TRUE
TRUE | TRUE | FALSE
out  NAND(in1, in2)
Can be used to build any circut

## Slide 11: Destructive Computation
In our gates, we always load the “in” addresses
Loading an address sets its value to True
  We can only use an address as input once
  After that, its value is destroyed
How can we build complex gates that require reusing the same value multiple times?

## Slide 12: Multiple output NAND (fan out)
if (*in1 + *in2 == 0)
return;
t = delay()
a = *(out1 + t)
a = *(out2 + t)
...
a = *(outn + t)
Load *in1
Load *in2
Delay
branch
Load *out1
Load *out2

## Slide 13: Minority Report
if (*in1 + *in2 == 0)
return;
if (*in2 + *in3 == 0)
return;
if (*in1 + *in3 == 0)
return;
a = *out
*in1 | *in2 | *in3 | *out
FALSE | FALSE | FALSE | TRUE
FALSE | FALSE | TRUE | TRUE
FALSE | TRUE | FALSE | TRUE
FALSE | TRUE | TRUE | FALSE
TRUE | FALSE | FALSE | TRUE
TRUE | FALSE | TRUE | FALSE
TRUE | TRUE | FALSE | FALSE
TRUE | TRUE | TRUE | FALSE
out  NOT(MAJ(in1, in2, in3))
Error Correction

## Slide 14: Circuits
4-bit ALU
  1258 gates, 84-95% accuracy
SHA-1
  One round: 2208 gates, 95% accuracy (67% with prefetcher)
  Full (two blocks, with repetitions) 95% accuracy
Game of Life
  7807 gates 73% accuracy for one generation, 25% for 20

## Slide 15: Flush+Reload on Square-and-Multiply
40ns
Typical Clock Rates
Chrome 0.1ms
Safari 1ms
Firefox 2ms
TOR 100ms
Apple M1 42 ns

## Slide 16: Reducing Timer Resolution
Measure this
With this

## Slide 17: Overcome Low Res Timers with Amplification
A NOT gate with a large fan-out amplifies the signal by a factor of 8
  Two layers – 64
  Three layers – 512
  Four layers – 4096
Amplify to a resolution of 0.1 second
if (*in == 0)
return;
a = *out1 + *out2 +
*out3 + *out4 +
*out5 + *out6 +
*out7 + *out8;

## Slide 18: Amplification is half the job
40ns
25us

## Slide 19: Prime+Store: High Resolution Prime+Probe
Prime+Probe is basically a NAND gate applied on the eviction set
Repeatedly probe our eviction set (apply a NAND gate)
  Store each result in a different output address
  Don’t measure the result
Amplify later
  Decouples probing from time measurements
Attack square-and-multiply ElGamal with a 0.1ms clock

## Slide 20: How Fast can we Probe?

## Slide 21: How fast can we probe?
Probing the cache takes time
Limited temporal resolution
  Thousands of cycles
Prime+Scope (CCS 2021) – 70 cycles.
Requires only one access to L1 cache.

## Slide 22: Prime+Scope code
uint32_t scope(char * address) {
uint32_t start = rdtscp();
char t = *address;
uint32_t end = rdtscp();
return end – start;
}
30 cycles
30 cycles
5 cycles
5 cycles
Measuring time is an order of magnitude slower than a cache access

## Slide 23: Using Prime+Store
Prime+Store is a hammer – let’s try it on this nail.
Result: 150 cycles – branch training is not cheap
Prime+Store with RET-based gates: 48 cycles.
48 < 70 Yay!
48 is still very slow

## Slide 24: Tapped multi-probed gates
Load *in
Delay
Load *o3
return
Delay
Load *o2
Load *in
Load *in
Delay
Load *o2

## Slide 25: Tapped multi-probed gates
Load *in
Delay
Load *o3
return
Delay
Load *o2
Load *in
Load *in
Delay
Load *o2

## Slide 26: Tapped multi-probed gates
Load *in
Delay
Load *o3
return
Delay
Load *o2
Load *in
Load *in
Delay
Load *o2

## Slide 27: 5 Cycles Measurement resolution

## Slide 28: Attacking S-Box based AES
S-Box based implementations are harder to attack
  Only 4 cache lines, and more accesses
Need to distinguish precise AES round
  Each rounds takes approximately 70 cycles
  Need sample rate faster than 35 cycles!
Prior works need either
  Non-trivial OS control
  Utilize the deprecated Intel TSX
  Modify the original code

## Slide 29: Attacking S-Box based AES
Need to measure exact round, i.e., exact time from start of AES
  Try to measure diff from code at start of AES – too noisy
  Instead measure diff between accesses to two S-Box cache lines

## Slide 30: Attacking S-Box based AES
Full key recovery of AES128 using Spec-o-Scope
Requires ≈10,000 traces
Collected in less than 3 seconds

## Slide 31: Summary
Microarchitectural weird machines are a thing
Can have security impact
New emerging area – much work to do