## Slide 1: Is Your Bluetooth Chip Leaking Secrets via RF Signals?
Yanning Ji, Elena Dubrova, Ruize Wang
School of Electrical Engineering and Computer Science
Royal Institute of Technology (KTH), Stockholm, Sweden

## Slide 2: Introduction
Motivation:
  Millions of Bluetooth-enabled devices use cryptographic accelerators. Are they leaking secrets?
Key contribution:
  We demonstrate the first attack on a Bluetooth chip’s hardware AES accelerator via RF side channel
Why RF side channel matters?
  No physical modification of device  No tamper-evidence
  Remote attack

## Slide 3: Prior RF side-channel attacks
Screaming channels attack (CCS'18):
  Extracted encryption key from software AES via RF
    Tiny AES in Cortex-M4 processor in a mixed-signal chip
 | Method | Distance | Environment | #Avg. | Enum. | #Traces
CCS’18 | Template | 10m | Anechoic chamber | 500 | No | 1428
 |  | 1m | Office |  |  | 52589
CHES’20 | Template | 15m | Office | 1000 | 223 | 5000
ASHES’20 | DL | 15m | Office | 100 | No | 11
 |  |  |  | 10 |  | 48
CPSS’21 |  |  |  | 1 |  | 341

## Slide 4: Limitations of prior work
Could not break hardware AES accelerator
  Fully parallel implementation in Counter with CBC-MAC (CCM) authenticated encryption mode
  Runs at 16 MHz, different from the Cortex-M4 64 MHz clock
Our research question:
  Can encryption key of AES accelerator be extracted via RF?

## Slide 5: Why mixed-signal circuits may leak secrets via RF?

## Slide 6: Why mixed-signal circuits may leak secrets via RF?
Analog part
Digital part
Other digital blocks
Bus
Digital-to-Analog Converter
RF block
Voltage-
Controlled Oscillator
HW AES block
CPU core
Substrate
coupling
①
②
③
Capacitive
coupling
RF signal generated by VCO may be affected
Current fluctuations in digital circuits induce noise in the shared silicon substrate, affecting analog components
Notes: VCO generates an RF signal at a frequency determined by an input control voltage

## Slide 7: Attack setup
Target:
  Nordic Semiconductor nRF52832 Bluetooth system-on-chip
Measurement setup:
  Antenna at 1m distance captures RF signals
  Software-defined radio demodulates RF signals at 2.4GHz + n16 MHz
Bluetooth band frequency
HW AES clock frequency

## Slide 8: Key recovery methods
Correlation analysis (CA), non-profiled attack
Deep learning (DL), profiled attack
Plaintext, 16 bytes
Key, 16 bytes
SubBytes
ShiftRow
MixColumn
AddRoundKey
…
Round 1
SubBytes
ShiftRow
MixColumn
AddRoundKey
Round 9
SubBytes
ShiftRow
AddRoundKey
Round 10
Ciphertext, 16 bytes
Attack point
Counter 1 encryption

## Slide 9: AES-CCM authenticated encryption mode
AES
Counter block 0
+
Ciphertext block 0
CMAC
MAC
Keystream S0
AES
Counter block 1
+
Ciphertext block 1
C1
Plaintext block 1
Keystream S1
...
Key K
Counter (CTR) mode
Cipher Block Chaining (CBC)-MAC mode
AES
+
IV
B0
AES
+
B1
K
K
K
AES
+
Bn
K
MAC
32-bit
...
Attack point

## Slide 10: Results for 180,000 traces (18.9 days of capture)
RWC’2025
Capture method | Key # | Device # | Attack method | # Incorrect key bytes, k | # Enum. | Enum. time
Cable | Key 1 | Device 1 | CA | 2 | 222.9 | 0.1 sec
 | Key 2 | Device 2 | CA | 2 | 222.9 | 0.1 sec
Antenna | Key 1 | Device 1 | CA | 3 | 233.1 | 92.1 sec
 | Key 2 | Device 2 | CA | 4 | 242.8 | 21.7 hrs
For CA attack, postions of incorrect bytes are unknown  #Enum. = 28k

## Slide 11: Results for 180,000 traces (18.9 days of capture)
Capture method | Key # | Device # | Attack method | # Incorrect key bytes, k | # Enum. | Enum. time
Cable | Key 1 | Device 1 | CA | 2 | 222.9 | 0.1 sec
 |  |  | DL | 0 | 0 | 0
 | Key 2 | Device 2 | CA | 2 | 222.9 | 0.1 sec
 |  |  | DL | 0 | 0 | 0
Antenna | Key 1 | Device 1 | CA | 3 | 233.1 | 92.1 sec
 |  |  | DL | 1 | 28 | 0.003 ms
 | Key 2 | Device 2 | CA | 4 | 242.8 | 21.7 hrs
 |  |  | DL | 1 | 28 | 0.003 ms
For CA attack, postions of incorrect bytes are unknown  #Enum. = 28k
For DL attack, postions of incorrect bytes are known  #Enum. = 28k

## Slide 12: Results for 90,000 traces (9.4 days of capture)
RWC’2025
Capture method | Key # | Device # | Attack method | # Incorrect key bytes, k | # Enum. | Enum. time
Cable | Key 1 | Device 1 | CA | 2 | 222.9 | 0.1 sec
 | Key 2 | Device 2 | CA | 3 | 233.2 | 92.1 sec
Antenna | Key 1 | Device 1 | CA | 7 | 267.4 | -
 | Key 2 | Device 2 | CA | 8 | 277.7 | -

## Slide 13: Results for 90,000 traces (9.4 days of capture)
Capture method | Key # | Device # | Attack method | # Incorrect key bytes, k | # Enum. | Enum. time
Cable | Key 1 | Device 1 | CA | 2 | 222.9 | 0.1 sec
 |  |  | DA | 0 | 0 | 0
 | Key 2 | Device 2 | CA | 3 | 233.2 | 92.1 sec
 |  |  | DA | 0 | 0 | 0
Antenna | Key 1 | Device 1 | CA | 7 | 267.4 | -
 |  |  | DA | 1 | 28 | 0.003 ms
 | Key 2 | Device 2 | CA | 8 | 277.7 | -
 |  |  | DA | 1 | 28 | 0.003 ms

## Slide 14: Results for 45,000 traces (4.7 days of capture)
RWC’2025
Capture method | Key # | Device # | Attack method | # Incorrect key bytes, k | # Enum. | Enum. time
Cable | Key 1 | Device 1 | CA | 4 | 242.8 | 21.7 hrs
 | Key 2 | Device 2 | CA | 5 | 252.1 | 1.53 yrs
Antenna | Key 1 | Device 1 | CA | 11 | 2102.1 | -
 | Key 2 | Device 2 | CA | 12 | 2106.8 | -

## Slide 15: Results for 45,000 traces (4.7 days of capture)
Capture method | Key # | Device # | Attack method | # Incorrect key bytes, k | # Enum. | Enum. time
Cable | Key 1 | Device 1 | CA | 4 | 242.8 | 21.7 hrs
 |  |  | DL | 1 | 28 | 0.003 ms
 | Key 2 | Device 2 | CA | 5 | 252.1 | 1.53 yrs
 |  |  | DL | 2 | 216 | 0.66 ms
Antenna | Key 1 | Device 1 | CA | 11 | 2102.1 | -
 |  |  | DL | 2 | 216 | 0.66 ms
 | Key 2 | Device 2 | CA | 12 | 2106.8 | -
 |  |  | DL | 2 | 216 | 0.66 ms

## Slide 16: Mitigation strategies

## Slide 17: Mitigation strategies
  Circuit-level: Reduce coupling between the digital and analog parts of a mixed-signal circuit at the design stage
    Use layout optimization and isolation techniques
  Algorithm-level: Apply countermeasures
  Masking (randomize intermediate states)
  Shuffling (randomize execution order)
  Clock randomization with duplication
  Protocol-level:
    Update key frequently
    Force fresh nonce for each encryption

## Slide 18: Ethical considerations
Responsible disclosure:
  Notified Nordic Semiconductor before publication
  Provided our scripts and data for independent evaluation

## Slide 19: Summary
Main contribution:
  First successful RF-based side-channel attack on AES-CCM hardware accelerator
Security implications:
  Attack is challenging but feasible with sufficient resources
  Not limited to Bluetooth devices
Key takeaway:
  Need proactive defenses against RF-based side-channel attacks before they scale

## Slide 20
Thank you!
20